## Slide 1
RC TRAILER JACK
Remote Control Trailer Wheel System
EECS 4020 Senior Design Project II
University of Toledo — College of Engineering
TEAM MEMBERS
MH
Mark Halter
Hardware Lead
JT
Jacob Thaxton
Hardware Engineer
SS
Shubh Shahra
Software Engineer
K
Kanisha
Software Engineer
📸 PROJECT PHOTO
(Insert photo of RC Trailer Jack)
Motorized remote-controlled trailer jack — replacing manual labor with smart engineering.
2026 Senior Design Project Competition | Group 7

## Slide 2
THE CLIENT & THE PROBLEM
Slide 2 of 7
👤 THE CLIENT
Recreational & commercial trailer owners
Anyone who regularly parks, positions, or hitches trailers — campers, boaters, farmers, and logistics operators.
Pain point:
The process requires precise maneuvering, often done alone, and is physically demanding and time-consuming.
⚠️ THE PROBLEM
1
Manual trailer jacks require significant physical effort
2
Positioning accuracy is difficult without a second person
3
Hitching requires constant back-and-forth movement
4
Risk of injury from excessive manual cranking
5
No feedback on alignment during maneuvering
RC Trailer Jack | EECS 4020 Senior Design | University of Toledo

## Slide 3
OUR INNOVATIVE SOLUTION
A smartphone-controlled motorized trailer jack that eliminates manual labor
🔧
HARDWARE
Motorized trailer jack using CIM 24VDC geared motors with Cytron SmartDriveDuo motor driver — providing precise control of movement and braking.
📱
SOFTWARE APP
Android mobile app with real-time steering, throttle, brake, and gear control. Camera-assisted UI for safe maneuvering with live connection feedback.
📡
WIRELESS LINK
BLE (Bluetooth Low Energy) enables low-latency motor commands from smartphone to ESP32 microcontroller with automatic safety stop on signal loss.
🔍 KEEN 3C — Curiosity: We questioned why trailer hitching hadn't been modernized — and explored a wireless solution nobody had built.

## Slide 4
HARDWARE DESIGN
Slide 4 of 7
SYSTEM ARCHITECTURE
📱 Smartphone
(Android App)
📡 ESP32
(BLE + Control)
⚙️ Motor Driver
(Cytron MDDS30)
🔧 CIM Motors
(24VDC Geared)
KEY COMPONENTS
Haul-Master 1000lb Swing-Away Trailer Jack
Primary load-bearing structure
CIM CM808-029F/E 24VDC Geared Motors
High-torque actuation
Cytron SmartDriveDuo MDDS30
Dual-channel motor driver with built-in test mode
ESP-WROOM-32 + Breakout Board Shield
BLE & Wi-Fi microcontroller with terminal adapter
Step-Down Voltage Converter
Battery → 3.3V rail for ESP32
8.7"×6.7"×4.3" Junction Box
Weather-resistant electronics enclosure
RC Trailer Jack | EECS 4020 Senior Design | University of Toledo

## Slide 5
SOFTWARE & APP DESIGN
Android application with BLE communication and real-time camera feed
🎮
Real-Time Controls
Steering, throttle, brake, and gear selection — all from the user's smartphone.
📶
BLE Communication
Low-latency Bluetooth connection with structured command packet transmission.
📸
Camera Feed
Live rear-view camera stream via Wi-Fi for assisted maneuvering.
⚡
Gradual Acceleration
Adjustable throttle with ramp-up logic for smooth and safe movement.
🛑
Safety Stop
Automatic motor halt on brake press or BLE signal loss — prevents accidents.
📊
Live TX/RX Status
Real-time connection indicators and transmission feedback in the UI.
🔗 KEEN 3C — Connections: We integrated hardware, firmware, Bluetooth protocols, and mobile app development — drawing from multiple engineering disciplines.

## Slide 6
RESULTS & DEMONSTRATION
Slide 6 of 7
100%
Wireless
Control
BLE
Low-Latency
Protocol
Live
Camera
Feed
Auto
Safety
Stop
WHAT WE ACHIEVED
✓
Successfully built and tested an Android app for wireless trailer jack control over BLE
✓
Implemented real-time steering, throttle, brake, and gear command transmission to ESP32
✓
Verified motor driver functionality and attached to full mechanical assembly on trailer
✓
Camera-assisted interface provides live rear-view feed for safe repositioning
✓
Safety stop engages automatically on brake or signal loss — validated in testing
✓
Full system tested on mock trailer; subsequent testing confirmed function on real full-scale trailer
RC Trailer Jack | EECS 4020 Senior Design | University of Toledo

## Slide 7
VALUE CREATED & FUTURE VISION
Creating real value for trailer owners through smart engineering
THE KEEN 3Cs IN ACTION
🔍 CURIOSITY
We challenged the status quo — why is trailer positioning still manual? We explored wireless control, BLE protocols, and mobile-first interfaces as unexplored solutions.
🔗 CONNECTIONS
We synthesized electrical engineering, embedded firmware (ESP32), mobile app development, and mechanical integration — drawing connections across disciplines.
💡 CREATING VALUE
We delivered measurable value: reduced labor, improved safety, one-person trailer operation, and a platform extensible to automated hitching and self-parking.
FUTURE IMPROVEMENTS
🤖
Self-Parking Mode
Automated trailer positioning using sensor feedback and path planning algorithms.
🎯
Auto-Hitch Setup
Automated hitching sequence aligns trailer to tow vehicle with precision sensors.
🔌
Multi-Trailer Support
Compatibility with various trailer styles and jack types for broader market reach.
📦
Compact Redesign
Miniaturized electronics enclosure and optimized motor placement for commercial viability.
Thank You | Advisor: Dr. Daniel Georgiev | Professor: Dr. Ashish Kharel | TA: Mehzabien Iqbal